## Slide 2
Type of hemodialysis
ارائه‌دهنده:
دکتر زهرا ایروانی
استادیار گروه نفرولوژی
مرداد 1405
کنفرانس علمی مداخلات درمانی در بیماران دیالیز
دانشگاه علوم پزشکی اصفهان

## Slide 3
MECHANISMS OF SOLUTE TRANSPORT
1
Diffusion:
The movement of solutes through a semi-permeable membrane from an area of higher concentration to an area of lower concentration
The movement result of random molecular motion.
Rate of Small molecules transport through the membrane will be high.
Large molecules, will diffuse through the membrane slowly
/ 24

## Slide 4
MECHANISMS OF SOLUTE TRANSPORT
2
Ultrafiltration (convective transport):
Movement of fluid along pressure gradians across the semi-permable membrane
Larger and smaller Solutes can pass easily through the membrane with the water (solvent drag).
/ 24

## Slide 6
List of titles
Intermittent hemodialysis : IHD
prolonged intermittent renal replacement therapy: PIRRT
Sustained low-efficiency hemodialysis : SLED
Continuous Renal Replacement Therapies: CRRT
Continuous hemodialysis : CHD
Continuous hemofiltration : C-HF
Slow continuous hemodiafiltration : C-HDF
Slow continuous ultrafiltration : SCUF
/ 24
4

## Slide 7
Intermittent Hemodialysis
5
/ 24
Hemodialysis:
Most common form of dialysis.
Removes blood from the body by a machine through a dialysis access.
Diffusion and ultrafiltration happens in dialyzer.

## Slide 8
ihd
6
/ 24
IHD sessions are typically prescribed:
Three times weekly
Lasting 3 to 4 hours each
Blood flow rates of 300 to 500 mL/min
Dialysate flow rates of 500 to 800 mL/min
Ultrafiltration removes excess fluid, and solute clearance mainly relies on diffusion

## Slide 9
Advantages of ihd
7
/ 24
Widespread availability
Low cost of disposables
Delivery with no anticoagulation usually feasible
Most rapid instantaneous clearance
May be performed with catheter or arteriovenous fistula or graft
Lowest rate of hypophosphatemia
Time off KRT allows more time for physical therapy relative to CRRT
IHD is preferred for rapid correction of electrolyte imbalances and drug intoxications due to its rapid solute removal

## Slide 10
disAdvantages of ihd
8
/ 24
Likely highest risk of hypotension
Likely highest risk of exacerbating intracranial hypertension
Limited fluid removal
Often requires limitation in dietary potassium or phosphate intake

## Slide 11
SLED
9
/ 24
SLED is a form of IHD using:
Extended (6- to 10-hour) session length
Reduced blood and dialysate flow rates.
Blood flow rates are about 150 to 200 mL/min
Dialysate flow rate is 100 to 300 mL/min.
The same machine used for IHD often can be used for SLED.
SLED allows units where CKRT equipment or personnel are unavailable, achieve similar benefits as CKRT.

## Slide 12
crrt
10
/ 24
CRRT uses diffusion, convection, or a combination to remove solutes and fluids gradually.
KDIGO Guidelines for AKI suggest that clinicians use CKRT for:
Hemodynamically unstable patients
septic patients
In patients with:
Acute brain injury or
Other causes of increase intracranial pressure or
Generalized brain edema

## Slide 13
Potential Advantages of Slow Continuous Therapies
11
/ 24
Continious therapies:
1.Hemodynamically well tolerated; smaller change in plasma osmolality
2.Better control of azotemia and electrolyte and acid-base balance
3.Highly effective in removing fluid (postsurgery, pulmonary edema, ARDS)
4.Facilitates administration of parenteral nutrition and obligatory intravenous medications by creating unlimited “space”
5.Less effect on intracranial pressure
6.User-friendly machines available

## Slide 14
C-HD
12
/ 24
The standard dialysis solution inflow rate is about 20 to 25 mL/kg/h.
The blood flow rate should be at least 3 times the dialysate flow rate.
At this slow blood flow rate and high blood-to-dialysate flow ratio, the outflow dialysate is almost 100% saturated with urea and other small-MW solutes.

## Slide 15
C-HF
13
/ 24
C-HF is a purely convection-based blood cleansing technique.
As blood flows through the hemofilter, a transmembrane pressure gradient between the blood compartment and the ultrafiltrate compartment causes plasma water to be filtered across the highly permeable membrane. As the water crosses the membrane, it sweeps along with it (nonprotein-bound) small and large molecules (pore size permitting) and remove them from the blood.
The removed ultrafiltrate is replaced by a balanced electrolyte solution infused into either the inflow (predilution) or the outflow (postdilution) line of the hemofilter.

## Slide 17
Filtration fraction
15
/ 24
This is the fraction of plasma flowing through the hemofilter that is removed and should be kept at 25% or lower to avoid overconcentration of red cells and plasma proteins in the hemofilter.
Overconcentration results in fouling of the membrane pores, which can impair ultrafiltration efficiency and lower the sieving coefficient, and overconcentration can also increase the likelihood of clotting.
When a high replacement fluid infusion rate in postdilution mode is desired, the blood flow rate needs to be increased above the usual 150 mL/min.

## Slide 18
Predilution mode
16
/ 24
We recommend using predilution whenever:
It is desirable to remove more than 25 L/d.
If the baseline blood viscosity is elevated (eg, if the hematocrit is >35%).
A slight lowering of the urea concentration of ultrafiltrate (usually to 80%-90% of the corresponding plasma value), but this small amount of dilution is outweighed by the ability to deliver an increased replacement solution infusion rate, enhancing overall middle-molecule clearances.
A combination of pre- and postdilution has been advocated by some practitioners.

## Slide 19
Small- versus middle-MW solute removal
17
/ 24
With CHD: larger-MW substances diffuse slowly in solution and thus have a lower rate of diffusive transfer across the dialyzer membrane.
With C-HF: convective removal rates of small- and larger-MW solutes are similar.
Hence, C-HF is more efficient than C-HD in terms of larger-MW toxin removal, including peptides, certain antibiotics, and vitamin B12.
But using a high replacement fluid flow rate with a small hemofilter can not increase the removal of larger, middle molecules.

## Slide 20
Venovenous blood access
18
/ 24
A dual-lumen cannula inserted into a large (internal jugular or femoral) vein.
The 2012 KDIGO AKI guidelines recommend using uncuffed venous catheters for CRRT
Use of longer (20-24 cm) soft, silicone temporary catheters for CKRT targeting placement of the catheter tip near the right atrium versus shorter (15-20 cm) catheters were associated with longer filter life and improved dose of therapy.

## Slide 21
Filter surface area and size
19
/ 24
The size of the filter should take the blood flow rate into account.
When large filters are used at low blood flow rates, the risk of clotting may be increased and Flow velocity through each fiber will be slow.
Use of a larger-size filter might be considered when removal of larger-MW solutes is desired and a high replacement fluid rate is to be used.

## Slide 22
CRRT fluids
20
/ 24
Premixed as commercially prepared sterile solutions.
They are typically packaged in 2.5-L or 5-L bags
Lactate or bicarbonate based solutions : The 2012 KDIGO AKI guidelines suggest using bicarbonate based solutions for all patients with AKI , more strongly for patients with liver failure and/or lactic acidosis and for patients in circulatory shock.
Citrate-based solutions. These fluids evolved from attempts to merge the buffering and anticoagulation properties of citrate.
Sodium , potassium, phosphate, calcium and Mg and glucose.

## Slide 23
ISOLATED ULTRAFILTRATION AND SCUF
21
/ 24
Isolated ultrafiltration is achieved using standard dialysis equipment by simply putting the dialysate in bypass and can be performed prior to dialysis, after dialysis, or independently of dialysis.
SCUF is achieved using the same circuitry as for C-HD but omitting dialysis solution. It is used primarily in an ICU setting to remove excess fluid from patients in whom residual kidney function is substantial and in whom electrolyte and acid-base imbalances are not an issue (refractory heart failure and mildly impaired kidney function)

## Slide 25
cerebral edema
22
/ 24
C-HF and C-HD systems with tight volumetric control should be used.
If possible, anticoagulation should be avoided.
Dialysis or replacement fluid should have a relatively higher sodium (>140 mM) and a lower bicarbonate (30 mM) concentration.
In severe cases of uncontrolled intracranial pressure, cooling of the dialysis or replacement solutions may be helpful, in addition to other measures used to cool the patient to 32 °C to 33 °C. At these temperatures, cranial oxygen demands are reduced.

## Slide 26
Sepsis and multiorgan failure
23
/ 24
Many centers will treat septic patients with C-HDF to increase removal of potential sepsis-mediating molecules (proinflammatory (TNF β, thromboxane B2, platelet activating factor) and anti-inflammatory mediators (IL-10) while retaining the effciency associated with use of dialysis.
Using a clearance dose of 35 mL/kg/h and dividing equally between dialysis and hemofiltration is a common strategy

## Slide 27
Other indications
24
/ 24
Acute lung injury and ARDS: Respiratory improvement appears to be due more to the volume removal effect rather than to the removal of inflammatory mediators.
Intoxication with dialyzable or filter-permeable drugs or toxins: especially when there is a risk of rebound in serum concentrations of the drug or toxin after IHD.

## Slide 28
chronic hemodialysis
3
/ 24
Choose
Thanks for your attention