## Slide 1: Physiologic Principles and Urea Kinetic Modeling
Shahram Taheri M.D.
Associate Prof.
Internist, Nephrologist
IUMS

## Slide 2: Introduction
Dialysis is a process whereby the solute composition of a solution, A, is altered by exposing solution A to a second solution, B, through a semipermeable membrane.
Conceptually, one can view the semipermeable membrane as a sheet perforated by holes or pores.

## Slide 3: Introduction
Water molecules and low-molecular-weight solutes in the two solutions can pass through the membrane pores and intermingle, but larger solutes (such as proteins) cannot pass through the semipermeable barrier, and the quantities of high-molecular-weight solutes on either side of the membrane will remain unchanged.

## Slide 4: MECHANISMS OF SOLUTE TRANSPORT
A. Diffusion
B. Ultrafiltration (convective transport)

## Slide 5: Diffusion
The movement of solutes by diffusion is the result of random molecular motion.
The larger the molecular weight of a solute, the slower will be its rate of transport across a semipermeable membrane.

## Slide 6: Diffusion
Small molecules, moving about at high velocity, will collide with the membrane often, and their rate of diffusive transport through the membrane will be high.
Large molecules, even those that can fit easily through the membrane pores, will diffuse through the membrane slowly because they will be moving about at low velocity and colliding with the membrane infrequently

## Slide 8: Ultrafiltration (convective transport)
Water molecules are extremely small and can pass through all semipermeable membranes.
Ultrafiltration occurs when water driven by either a hydrostatic or an osmotic force is pushed through the membrane.
Those solutes that can pass easily through the membrane pores are swept along with the water (a process called “solvent drag”).
The water being pushed through the membrane is accompanied by such solutes at close to their original concentrations.

## Slide 10: Hydrostatic ultrafiltration
Transmembrane pressure:
  During hemodialysis, water (along with small solutes) moves from the blood to dialysate in the dialyzer as a result of a hydrostatic pressure gradient between the blood and dialysate compartments.
  The rate of ultrafiltration will depend on the total pressure difference across the membrane (calculated as the pressure in the blood compartment minus the pressure in the dialysate compartment).

## Slide 11: Hydrostatic ultrafiltration
Ultrafiltration coefficient (KUF):
  The permeability of dialyzer membranes to water, though high, can vary considerably and is a function of membrane thickness and pore size.
  The permeability of a membrane to water is indicated by its ultrafiltration coefficient, KUF.
  KUF is defined as the number of milliliters of fluid per hour that will be transferred across the membrane per mm Hg pressure gradient across the membrane.

## Slide 13: Purpose of ultrafiltration.
Typically, a patient being dialyzed thrice weekly will gain 1–4 kg of weight between treatments (most of it water), which will need to be removed during a 3–4-hour period of dialysis.
Patients with acute fluid overload may need more rapid fluid removal.
Thus, the clinical need for ultrafiltration usually ranges from 0.5 to 1.2 L/hr.

## Slide 15: SOLUTE REMOVAL FROM THE PERSPECTIVE OF THE DIALYZER
When uremic blood is exposed to dialysis solution, the flux rate of these waste solutes from blood to dialysate is initially much greater than the back-flux from dialysate to blood.
Eventually, if the blood and dialysate were left in static contact with each other via the membrane, the concentration of permeable waste products in the dialysate would become equal to that in the blood, and no further net removal of waste products would occur.

## Slide 16: SOLUTE REMOVAL FROM THE PERSPECTIVE OF THE DIALYZER
In practice, during dialysis, concentration equilibrium is prevented, and the concentration gradient between blood and dialysate is maximized, by continuously refilling the dialysate compartment with fresh dialysis solution and by replacing dialyzed blood with undialyzed blood.

## Slide 17: SOLUTE REMOVAL FROM THE PERSPECTIVE OF THE DIALYZER
Normally, the direction of dialysis solution flow is opposite to the direction of blood flow.
The purpose of “countercurrent” flow is to maximize the concentration difference of waste products between blood and dialysate in all parts of the dialyzer.

## Slide 18: Extraction ratio.

## Slide 20: Concept of clearance

## Slide 22: The K0A, mass transfer area coefficient
If the extraction ratio remained constant at 60%, a doubling of the blood flow rate would double the clearance.
However, removal efficiency falls at higher blood flow rates, and so the clearance does not increase with QB in a 1:1 ratio.

## Slide 23: The K0A, mass transfer area coefficient
Ultimately, at very high blood flow rate, the clearance will plateau.
The theoretical maximum clearance of a dialyzer ( for a given solute) at infinite blood and dialysate flow rates is called the K0A and has units of mL/min.
For the dialyzer in Table 3.1, the K0A is close to 600 mL/min.

## Slide 24: The K0A, mass transfer area coefficient
The K0A also has a physical aspect.
It is the multiple of two quantities:
1.K0, the permeability coefficient of the dialyzer membrane for a given solute,
2.A, the total effective surface area of the membrane in the dialyzer.

## Slide 25: The K0A, mass transfer area coefficient
Doubling the surface area of the membrane in a dialyzer will roughly double the K0A.
Two dialyzers of the same surface area do not necessarily have the same K0A, as the K0 values of the membranes used in those dialyzers can be markedly different.
The K0 can be increased by making the membrane thinner, by adjusting its porosity, and by optimizing the fluid path of dialysate in the dialyzer using spacer yarns and other features.

## Slide 27: Effect of erythrocytes
In the concept of clearance described earlier, the blood was treated as a simple fluid.
At a hematocrit of 30%, a blood flow of 400 mL/min is really a plasma flow rate of 280 mL/min and an erythrocyte flow rate of 120 mL/min.
What is measured at the dialyzer inlet and outlet are the plasma levels of a given waste product.

## Slide 28: Effect of erythrocytes
For urea, the presence of erythrocytes is not a major problem because urea diffuses into and out of erythrocytes quickly outlet plasma urea nitrogen level is 40 mg/dL, the urea concentration in erythrocytes will have been reduced to about that level also.
For creatinine and phosphorus and many other solutes, the problem is more complex because these substances do not equilibrate quickly between plasma and erythrocytes.

## Slide 29: Effect of erythrocytes
In fact, very little creatinine or phosphorus is removed from red blood cells during passage through the dialyzer.
When calculating the removal rate of creatinine or phosphorus in mg/min or mmol/min, one needs to use the plasma flow rate instead of the blood flow rate.

## Slide 30: Effect of blood water
As noted, urea is dissolved in erythrocytes and plasma water and is removed from both during passage through the dialyzer.
Approximately 93% of plasma is water (depending on its protein concentration), and about 72% of an erythrocyte is water.
Some urea associates with the nonwater portion of erythrocytes.
On average, urea is dissolved in a volume that is about 86% of the blood.

## Slide 31: Effect of blood water
The correction for blood water becomes important when using the dialyzer clearance to compute how much urea is being removed during a dialysis session.
For solutes like creatinine and phosphorus that are removed from the plasma compartment only passage through the dialyzer, the volume of removal is about 93% of the plasma flow rate.

## Slide 32: Effect of blood water
Increasing the hematocrit (e.g., from 20% to 40%) causes only a trivial reduction of the blood water urea clearance but will be associated with a noticeable reduction in the clearance of creatinine or phosphorus, due to the effect of hematocrit on the plasma flow rate.

## Slide 33: Effect of dialysis solution flow rate
A faster dialysis solution flow rate increases the efficiency of diffusion of urea from blood to dialysate although the effect is usually modest.
The usual dialysis solution flow rate is 500 mL/min.
A flow rate of 800 mL/min will increase urea clearance by about 5%–8% when a high efficiency dialyzer is used and when the blood flow rate is greater than 350 mL/min.

## Slide 34: Effect of dialysis solution flow rate
On the other hand, in some daily, nocturnal, or intensive care unit (ICU)–based applications, dialysate flow rate is markedly lower than 500 mL/min.
The optimum dialysis solution flow rate is 1.5–2.0 times the blood flow rate.
Above that, the increase in efficiency is quite small, especially with some of the newer dialyzers where the dialysis solution flow path has been optimized.

## Slide 35: Effect of molecular weight on diffusive clearance
Because high molecular weight solutes move slowly through solutions, they diffuse poorly through the membrane.
As a result, the extraction ratio for molecules larger than urea will be less than that of urea; plus, to calculate clearance, this lower extraction ratio must be multiplied by the plasma flow rate, and not the blood flow rate.

## Slide 36: Very large molecules
Very large molecules, such as β2-microglobulin (MW 11,800), cannot get through the pores of standard (low-flux) dialysis membranes at all.
Thus, dialyzer clearance of β2-microglobulin will be zero! “High-flux” membranes have pores of sufficient size to pass this large molecule.
Also, some dialysis membranes remove β2-microglobulin by adsorption.

## Slide 37: Dialyzer efficiency versus flux
Dialyzer efficiency: Refer primarily to the ability of a dialyzer to remove small solutes.
The dialyzer efficiency is best represented by the K0A for urea.
The flux of a dialyzer refers to its ability to remove very large molecules such as β2- microglobulin.

## Slide 38: Dialyzer efficiency versus flux
There is no single measure in common use to specify the flux of a dialyzer, though water permeability (KUF) can be used.
Usually high-flux dialyzers will have a water permeability greater than 15–20 mL/hr per mm Hg.
One can have a small, low-efficiency (K0A = 400 mL/min) dialyzer that is high flux, or a high-efficiency dialyzer (K0A = 1,200 mL/min) that is low flux and that removes urea very well but that removes no β2-microglobulin.

## Slide 39: SOLUTE REMOVAL FROM THE PATIENT PERSPECTIVE
Urea generation occurs in proportion to protein breakdown as reflected in the protein nitrogen appearance (PNA) rate.
In stable patients, the PNA is proportional to dietary protein intake.

## Slide 40: SOLUTE REMOVAL FROM THE PATIENT PERSPECTIVE
Using a mathematical model known as urea kinetics, one can compute both the rate of removal and production of urea.
The extent of urea removal gives us a measure of the adequacy of dialysis, and the amount of urea nitrogen generation gives an estimate of dietary protein intake.

## Slide 41: The weekly serum urea nitrogen profile
The predialysis SUN level is typically reduced by about 70% so that postdialysis SUN is 30% of the predialysis value.
During the subsequent interdialytic period (assuming a thrice-weekly dialysis schedule), the SUN will rise to almost the same level as that seen prior to the first treatment.
The result is a sawtooth pattern.

## Slide 42: The weekly serum urea nitrogen profile
The time-averaged (TAC) SUN level can be computed mathematically as the area under the sawtooth curve divided by time.
Both the predialysis SUN and TAC SUN levels reflect the balance between urea production and removal.
For a given level of dialysis therapy, predialysis SUN and TAC SUN will rise if urea nitrogen generation (g) is increased and will fall if g is decreased.

## Slide 43: The weekly serum urea nitrogen profile
Also, for any given rate of urea nitrogen generation, predialysis SUN and TAC SUN levels will rise if the amount of dialysis is decreased or will fall if the amount of dialysis is increased.
Therapy was thought to be adequate as long as predialysis or TAC SUN was appropriately low.

## Slide 44: The weekly serum urea nitrogen profile
However, low predialysis or TAC SUN levels were found to be associated with a high mortality rate and were found to most often reflect inadequate protein intake rather than adequate dialysis.

## Slide 45: Indices of urea removal
Urea reduction ratio (URR). The current primary measure of dialysis adequacy is the treatment-related URR.
This is computed as follows: Assume that predialysis SUN is 60 mg/dL and postdialysis SUN is 18 mg/dL. The relative reduction in SUN (or urea) level is (60 − 18)/60 = 42/60 = 0.70.
By convention, URR is expressed as a percentage, so the value of the URR in this example would be 70%.

## Slide 46: Indices of urea removal
Kt/V urea:
The Kt/V urea is a dimensionless ratio representing volume of plasma cleared of urea (Kt) divided by the urea distribution volume (V).
K is the dialyzer blood water urea clearance (L/hr), t is dialysis session length (hours, hr), and V is the distribution volume of urea (liters, L), which is close to total body water.

## Slide 47: Indices of urea removal
If we deliver a Kt/V of 1.0, this implies that K × t, or the total volume of blood cleared during the dialysis session, is equal to V, the urea distribution volume.

## Slide 48: How URR is related to Kt/V.

## Slide 57
https://www.omnicalculator.com/health/kt-v
https://www.easycalculation.com/medical/dialysis.php

## Slide 58: Multipool models, urea inbound, and rebound.
Because urea is being removed from a smaller apparent volume during the early part of dialysis, the SUN during the initial part of dialysis falls more quickly than expected.
We have designated this unexpected early fall in SUN during the early stages of a dialysis session as urea inbound.

## Slide 60: Multipool models, urea inbound, and rebound.
Toward the end of dialysis, as a concentration gradient develops between the sequestered compartment and the accessible compartment, the fall in SUN slows.
After dialysis is complete, continued movement of urea from the sequestered to the accessible compartment causes the postdialysis urea rebound

## Slide 62: The concept of equilibrated Kt/V (eKt/V)
After dialysis, urea diffuses back from sequestered tissue sites into the blood to cause a postdialysis rebound, which is largely complete by 30–60 minutes.
One can measure the postdialysis SUN at this time and compute a “true” or equilibrated URR, which will be less than the URR based onan immediate postdialysis sample.
The equilibrated URR can be translated into an equilibrated Kt/V.

## Slide 63: The concept of equilibrated Kt/V (eKt/V)
The amount of urea rebound depends on the intensity or rate of dialysis that was given relative to body size.
The rate of dialysis can be expressed as the number of Kt/V units per hour, or (Kt/V) divided by t in hours.
Based on urea modeling, a formula modified from one suggested by Tatersall (1996) can be used to predict the amount of rebound based on the rate of dialysis:

## Slide 66: ACCESS RECIRCULATION
Normally blood flow through an AV access averages about 1 L / min.
The blood pump, which normally routes a portion of this flow through the dialyzer, usually is set to take a flow of 350–500 mL/min.

## Slide 67: ACCESS RECIRCULATION
Because flow through the vascular access normally exceeds the demand of the blood pump, usually all of the blood coming into the blood pump is coming from the access
The urea concentration of blood entering the dialyzer is the same as that in the upstream access, and there is no access recirculation

## Slide 69: ACCESS RECIRCULATION
In a failing AV graft or fistula, flow through the access can decrease markedly, to 350–500 mL/min or slower.
In such circumstances, part of the flow leaving the dialyzer reverses flow through the access and reenters the dialyzer.
Then the dialyzer inlet blood becomes admixed, or “diluted,” with dialyzer outlet blood.

## Slide 70: Impact of access recirculation on dialysis adequacy
When access recirculation occurs, the urea concentration in the blood entering the dialyzer may be reduced by 5%–40% or more.
The amount of urea removed in the dialyzer is equal to the volume of blood cleared × dialyzer inflow urea concentration.
Although dialyzer clearance remains unchanged, the amount of urea removed is reduced because the concentration of urea entering the dialyzer inlet is reduce

## Slide 71: Impact of access recirculation on dialysis adequacy
In patients with access recirculation, if blood at the end of dialysis is drawn from the dialyzer inlet blood line, the urea level in this blood will be lower than that in the patient’s upstream blood.
Hence, the apparent postdialysis SUN will be artifactually low, and the URR and, consequently, the spKt/V both will be overestimated.

## Slide 72: Avoiding the impact of access recirculation on URR or spKt/V
To ensure that blood being sampled reflects patient blood, one needs to slow the blood pump to a flow rate (e.g., 100 mL/min) that is assuredly below the access flow rate for a short period of time (10–20 seconds).
Lowering the blood flow stops the backward flow of blood from the dialyzer outlet to inlet and now all blood entering the arterial needle is upstream blood.

## Slide 73: Avoiding the impact of access recirculation on URR or spKt/V
The length of the slow-flow period depends on the dead space between the tip of the arterial needle and the sampling port
Postdialysis blood should always be drawn after a short slow-flow period for this reason.

## Slide 74: Avoiding the impact of access recirculation on URR or spKt/V
Another clever method of avoiding this problem is to just shut off the dialysate flow for 3 minutes at the end of dialysis (or put dialysate flow into bypass) while letting the blood flow go full tilt.
After 3 minutes, the SUN level in the blood leaving the dialyzer is similar to that going in, and so the inlet SUN level now reflects the SUN level in the patient’s blood

## Slide 75: CARDIOPULMONARY RECIRCULATION
A recirculation can be defined broadly to occur whenever blood leaving the dialyzer outlet returns to the inlet without first having traversed the peripheral urea-rich tissues.
In access recirculation, the recirculation occurs via the short access segment between the venous and arterial needles.

## Slide 76: CARDIOPULMONARY RECIRCULATION
Cardiopulmonary recirculation occurs through the heart and lungs (which contain negligible amounts of urea) when the dialyzer is fed from the arterial circulation (e.g., via an AV access). During dialysis, cleared blood from the dialyzer outletreturns to the heart.

## Slide 77: Impact of cardiopulmonary recirculation on dialysis adequacy
Dialysis with an AV access is inherently less efficient (by about 5%–10%) than that using a venous access.
This effect usually is outweighed by the higher blood flow rates achievable with AV access and the avoidance of venous catheter-related access recirculation.

## Slide 78: MACHINE-ESTIMATED MEASURES OF HEMODIALYSIS ADEQUACY
Estimating dialyzer clearance by pulsing dialysate with sodium and analyzing resulting changes in dialysate conductivity.
UV absorbance of spent dialysate

## Slide 79: CARDIOPULMONARY RECIRCULATION
In the aorta, the cleared blood is partitioned; some of it gets routed to the nonaccess arteries that lead it to the tissues to pick up more urea, but a fraction goes directly back through the access to the dialyzer without having traversed aperipheral capillary bed.